## Slide 1
E Zhang
UAS Airport Ground Traffic Simulation for vision-based UAV ground Operation
MS Software Engineering
Embry-Riddle Aeronautical University

## Slide 2
Background
System Design
System Realization
Future Work

## Slide 3
Background
System Design
System Realization
Future Work

## Slide 4: Background
Background
  Runway safety is a top priority at both the Federal Aviation Administration (FAA) and the National Transportation Safety Board. Reducing collision on the airport field is a major component of the effort to improve runway safety for the benefit of all air travelers.
  During an UAS airport ground operation, the taxiing of an UAV can be done by a pilot sitting in the control room with the help of video feeds originated from the UAV being operated. This type of operation can be risky in busy UAS airports where other vehicles or obstacles may appear on the taxiway.
  We consider a new approach for this operation---using cameras mounted on the buildings at the UAS airport to monitor the situation of the ground operation in the UAS airport. However, the testing of the proposed approach is cumbersome, risky, and costly in real UAS airports.

## Slide 5: Background
Project purpose
  Provide a simulation of version-based ground operation system.
  Provide a simulation of the airport operation involving aircraft and airport traffic. (Create scenario for demonstration)
  Set up one or more camera on the airport tower or other building which used to monitor the aircraft movement. (Obtain the image data)
  With this information, The operation system will locate the aircraft and give feedback to control or steer the UAV on the runway. (Feedback Control UAV)

## Slide 6
Background
System Design
System Realization
Future Work

## Slide 7: System Design
Simulation - Unity3D
  Use Unity3D to provide simulation scenario.
    Abundant materials and Asset
    Suitable for quick development
    Multi-platform (support.NET )
Data Transmission - Named Pipe
  Use Named Pipe to complete data transmission.
    Named pipe (also known as a FIFO for its behavior) is an extension to the traditional pipe concept
    Inter-process communication - to transfer data between two process on one workstation
    Provides a separate conduit for client/server communication (Two - way)

## Slide 8: System Design (Continued)
Image processing - MatLab
  Use MatLab to process image data
    A very large (and growing) database of built-in algorithms and Toolbox for image processing and computer vision applications
    The ability to read in a wide variety of both common and domain-specific image formats
    The source code for all image processing functions are accessible for scrutiny and test

## Slide 9: System Design
Demonstration
  Environment picture
  Camera location
  Pipe Console & MatLab
  Video Demo

## Slide 10
Background
System Design
System Realization
Future Work

## Slide 11: System Realization
Unity3D Simulation
  1. Path setting & generation
  2. UAV and vehicle control
  3. UAV and vehicle path planning
Named Pipe Translation
  1. Pipe Server
  2. Pipe Client
MatLab Image Process
  Image process

## Slide 12: System Realization
Unity3D Simulation
  1. Path setting & generation

## Slide 13: System Realization
Unity3D Simulation
  1. Path setting & generation
    Input: Way points position Output: Smooth path way points
      Get every point position & distance to the start point;
      Divide total distance into several parts based on smooth parameter (bigger = smoother)
      For each part distance (equal to each path way point)
        Get two nearest setting way point
        Find interpolations value between two points
        Get two more surrounding points
        Calculate smooth path way point
      Return all path way points

## Slide 14: System Realization
Unity3D Simulation
  1. Path setting & generation

## Slide 15: System Realization
Unity3D Simulation
  2. UAV and Vehicle control
    Wheel collider
    The Wheel Collider is a special collider for grounded vehicles. It has built-in collision detection, wheel physics, and a slip-based tire friction model. It can be used for objects other than wheels, but it is specifically designed for vehicles with wheels.

## Slide 16: System Realization
Unity3D Simulation
  2. UAV and Vehicle control
    Input: value of steer, acceleration, footbrake, handbrake Output: movement
      Set the steer on the front wheel
        Check if the wheel is on the ground
        Fix gimbal lock (suddenly shift direction) by changing car body’s moving direction
      Apply driving behavior
        Add thrust torque to the drive wheel
        Speed checking (keep under the Top speed)
      Traction control
        Check for driving wheels’ tire slip
        IF slip > threshold value & torque > 0
          Then torque reduce
          Else torque increase

## Slide 17: System Realization
Unity3D Simulation
  3. UAV and Vehicle path planning
    Way point tracker – based on path generation
    Input: generated path Output: moving tracker
      Get controlled object move speed
      For every frame set target to new position according to preset-ahead distance and move speed
      Update current progress distance and position

## Slide 18: System Realization
Unity3D Simulation
  3. UAV and Vehicle path planning
    Control AI – decide when to slow down
    Input: Control movement & target (waypoint tracker) Output: movement control
      Get distance and angle between target and current position
      Calculate cautiousness parameter according to distance and angle which decide the desire speed
      Calculate steering, acceleration, brake parameter based on angle, distance and desire speed
        Steering angle aim for the target
        Acceleration & brake depend on comparison between desire speed and current speed
      Apply movement control

## Slide 19: System Realization
Unity3D Simulation
    RESULT

## Slide 20: System Realization
Named Pipe Transmission
To implement name pipes, use the NamedPipeServerStream and NamedPipeClientStream classes in .NET Framework
  Pipe Server
    Create pipe server
      Create pipe server with name and transmission mode (InOut)
    While (pipe is connected)
    Get image data
      Read every pixels texture data of every camera in RGB format before rendering
      Get raw image data
      Change data structure, separate R/G/B into three array
    transfer data
      Transfer the size of picture (NamedPipeServerStream.writeByte())
      Transfer the R/ G/ B array (NamedPipeServerStream.write())
    Get distance data from client
      Read bytes form pipe client (.ReadByte())
    End & pipe.close()
Use reference - MATLAB COM(Component Object Model) object
  Pipe Client
    Create pipe client & connect to pipe server based on pipe name
    Create Matlab COM interface load local data (background)
    While (pipe is connected)
    Receive data from pipe server
      Get image size first
      Get image R/ G/ B array
      Check if the stream is null or correct
    Use Matlab function
      Invoke matlab function to process image data
    Send process result
    End & pipe.close()

## Slide 21: System Realization
MatLab Image Process
  Image data Process
    Input: R/G/B array & background image data Output: distance between two object
      Reshape R/G/B array into matrix [width, height] based on the picture size
      Reverse the R/G/B matrix and combine to full image matrix
      Use rgb2gray convert RGB image to gray image
      Process, get objects in the image
        Background – front
        Im2bw change to binary image
        Dilate and erode process (fulfill the hole)
        Select objects based on area
        Draw boundary
      Calculate distance based on objects’ boundaries
      Return distance

## Slide 22: System Realization
MatLab Image Process
  Result

## Slide 23
Background and Purpose
System Introduction
System Realization
Future Work

## Slide 24: Future Work
MatLab
Accuracy
Multiple Objects detection and Object identification
Named Pipe
Time manage based on Multiple threads of multiple pipes
Change to network transmission by using socket

## Slide 25: Questions